Coiled Mug and Free Coil– You will use this self-evaluation tool to provide one grade of 200 points for the two projects.

You will need to slab the base then coil the walls of the mug.  Then you will need to pull and attach a handle to this mug.  For the Mug you will attempt to replicate the example in the classroom.  For the Free Coil you will use the coiling technique to make a similar size coiled piece of ceramics.  For both coiled pieces you must sculpt something on the outside of the ceramic piece.

The mug should be about 4” high and use about 1-2lbs of clay.  The free form should use a similar amount of clay.  Make sure your base is at least 3/8 of an inch thick.  If it is too thin it will not survive the bisque fire and be hard to handle.  If it is too thick it will take a long time to dry and may cause the final product to be heavy.

When joining coils make sure you don’t capture any air between the coils (this can cause the pot to explode in the kiln).  Make sure the clay is not too dry.  If necessary add water to the seam.

When not working with these coiled projects make sure they are covered with plastic. Smooth the seams with a rib and make sure you are not loosing the shape of the coiled piece.

After you have finished the mug, look at the bottom (foot) and top (lip).  These are the starting and ending points of the form and should create a smooth transition into space.

Below is the self evaluation for this assignment.  After you have completed the project and rated yourself we will meet to finalize your points for this project.  Projects that are late will loose 5%.  More than 1 week late will loose 10%

Objective – Use coils to make pieces of ceramics.  Learn to pull a handle.

| Self Evaluation Form Assignment: Coiled Mug & Free Coil |  |
| --- | --- |
| Write in the box under “Your proposed rating” the number that best reflects how well you completed that criterion for the assignment | Excellent | Good | Average | Needs Improvement | Your proposed rating | Teacher’s Rating |
| Criteria 1 – How well was model duplicated or how creative was the free form project? How creative was the sculpting on the outside of the piece. | 40-36 | 35-32 | 31-28 | 27 or less |  |  |
| Criteria 2 – Were the seams smooth? Was there separations between coils (-5)? Did the handle stick (-5)? Did the piece survive the bisque fire? | 40-36 | 35-32 | 31-28 | 27 or less |  |  |
| Criteria 3 – How was the glaze applied? ? Did you use more than one glaze color? How clean were the glaze lines? | 40-36 | 35-32 | 31-28 | 27 or less |  |  |
| Criteria 4 – Effort: took time to develop idea & complete project? (Didn’t rush.) Good use of class time? | 40-36 | 35-32 | 31-28 | 27 or less |  |  |
| Criteria 5 – Craftsmanship – Neat, clean & complete? Skillful use of the ceramic tools? No sharp or rough edges. | 40-36 | 35-32 | 31-28 | 27 or less |  |  |
| Total: 200 |  |  |  |  |  |  | Teacher Total |

One Questions about this project? ____________________________________